History
Author	Rev	Date / Remark
S. Kabir	01	03/08/25 <Initial release>d

# Purpose
## This document serves as a technical reference for the home server setup running Proxmox 7.x+ The server functions as a private cloud, file server, and virtualization host without internet dependency.
# SCOPE
Tool #	Description
T201	Private data server.

# Requirements
## Hardware Requirements
Req #	Description	Test?	Test #
	Server Hardware (CPU , RAM, Storage) / Processor (CPU): At minimum of 6 cores and a clock speed of 2GHz that support CPU virtualization / Memory (RAM): / At least 16GB DDR4/DDR5 / Storage: At minimum 256GB with RAID for fault tolerance. / NIC: At least one gigabit Ethernet port / Graphics: Standard VGA or HDMI output for basic setup (Proxmox supports headless operation but may require a monitor during setup). / Peripheral I/O: At least two USB ports	Y	None
	Optionally, a managed network switch with at least 5 port	N
	Optionally, UPS for power backup	N
	Optionally, backup storage (External Drive)

## Software Requirements
Requirement #	Description	Test?	Test #
	The server must run on a virtualization environment such as Proxmox Virtual Environment must boot up without errors that may inhibit performance.	<Y/N>	<Test#>
	The server must provide a private / File sharing scheme such as SAMBA to offer network drives for mass storage. / Local cloud content collaboration platform such as Nextcloud. / Network print server to share printer within the LAN. / Network scanner server to share scanners within the LAN. / Docker host to run container applications.
	The server must provide a test environment which mimics similar test virtualization environment.
	Optionally, the server may provide a IT configuration automation tool such as Ansible.
	The server must use a predetermined set of static IP addresses to for its services. The router / switch DHCP settings must be configured suitably such that no IP conflict will occur.

# Equipment / Tools
## Equipment
### A flash drive of 16GB+(to create a boot able disk)
### A broadband internet connection
## Tools
### Software
#### Latest Proxmox LTE (.ISO) file
#### A bootable media creation tool such as Rufus
### <List all software(s)>
# Bill of materials
## A computer with suitable processing capabilities
## See BOM (Doc#)
## <Insert Bill of Materials>
# Procedure
## <Document detailed implementation steps, prerequisites, test, troubleshooting and routine maintenance procedure.>
## Preparing Server Hardware
### Connect a monitor to the server.
### Power up and enter into motherboard boot screen. In this case “Del” or “F2” button for Asrock brand motherboard.
### Setup below parameters.
Parameter Path	Parameter	Value / Action
Main	RTC
Advanced \ SVM Mode	CPU Virtualization
Advanced \ PCI Configuration	IO Virtualization
Advanced \ Onboard Devices Configuration	Turn On Onboard LED in S5	Enabled
	Restore Onboard LED Default	Disabled
	RGB LED On / OFF	Off
	Gnb Hd Audio	Enabled
	Front Panel	HD
	Restore On AC Power Loss	Power O
	Wi-Fi and WAN Radio	Disabled
	BT On / Off	Disabled
	PS2 Y-Cable	Auto
Advanced \ Storage Configuration	AHCI	None
Advanced \ ACPI Configuration	Suspend to RAM	Auto
	Deep Sleep	Disabled
	PS/2 Wakeup	Disabled
	RTC Alarm Power On	By OS
	USB PD in S5	Disabled
Advanced \ AMD CBS\ NBIO Common Options	IOMMU	Enabled
	DMA Protection	Auto
	DMAr Support	Auto
	PCIe ARI Support	Auto
	HD Audio Enable	Auto
Boot	Priority during OS installation	Need basis
OC Tweaker	Save User Profile in BIOS or Flash	Recommended, Production V1.0 PATH: TBD
Exit	Save Changes and Exit	Yes

### Bootable disk
#### Create bootable disk on a separate machine from the server OS ISO file.
### Install the OS
#### Insert the bootable flash drive on a server USB port and then reboot the server.
#### Boot from the flash device
#### Rest TBD.
## First Time Boot/ Setup:
## Setting up Ansible Control Node
### Ansible control node can be any computer that is connected to the same local network. Below setup is for Windows 10 machine WSL2. Windows 11 inherently supports WSL. If using a Linux machine, skip this.
#### Run “wsl2-install-win10.ps1” from “bash-scripts”. Launch Windows PowerShell in admin mode. May need to run below command to bypass security. Restart the computer for the changes take effect.
    Set-ExecutionPolicy -Scope Process -ExecutionPolicy Bypass
#### Check installation by running below command which should yield following.
wsl --list --verbose
  NAME STATE VERSION
* Ubuntu Stopped 2
  Debian Stopped
#### Here two version installed. To launch either, use below command.
wsl -d <DistroName>
#### Follow on screen instructions to setup account. It should by default have networking configured. Therefore it should have visibility to your local ` network and internet.
##### Note: WSL2 runs as a lightweight virtual machine using a Hyper-V-based virtual Ethernet adapter. WSL connects to a virtual gateway inside Windows, and Windows acts as a NAT router for it.
#### (Optional)Map a shared folder
sudo mkdir -p /mnt/<name of the drive>
sudo mount -t drvfs <drive_letter>: /mnt/<drive_letter>
#### Next, run setup-control-node.sh from the control node. But first, copy it to the control node and then make the script executable. Best practice is to copy it to the control node.
##### Note: The shared drives is not mounted automatically. Which can be done if necessary.
# Optional: create a target directory in WSL
mkdir -p ~/ansible/wsl
# Optional: Copy from the C:\ drive
cp /mnt/c/<actual_path>/setup-control-node.sh ~/ansible/wsl/
# Make it executable
chmod +x ~/ansible/wsl/setup-control-node.sh
# Run it
~/ansible/wsl/setup-control-node.sh
#### Ping main production server from WSL and then generate SSH key pair. Accept default path. Optionally, use pass phrase for added security.
##### Note: Last part is comment.
ssh-keygen -t rsa -b 4096 -f ~/.ssh/ansible_id_rsa_ansible-user -C "ansible-user@control_node"
#### Remove old keys for server from control node if needeed. It will throw error if the server has changed.
#### Note: Set temporarily “PasswordAuthentication yes” using nano /etc/ssh/sshd_config.
ssh-keygen -f "/home/rumie/.ssh/known_hosts" -R "192.168.0.111"
#### Next, copy the SSH public key to main prod server from control node. Now, Ansible utilize passwordless secure login.
//ssh-copy-id username@<main_prod_server_ip_addr>
#### To view the public key use below command
//cat ~/.ssh/id_ed25519.pub
#### Next, create users on the main production server using following command.
ansible-playbook playbooks/bootstrap.yml \

  -l pve_main \
  -u rumie \
  --ask-become-pass --check
ansible-playbook playbooks/validate-bootstrap.yml -l pve_main
#### SSH in to the main production server to allow passwordless sudo escalation for admins. Its safe since we are using SSH keys to login.
echo "prodadmin ALL=(ALL) NOPASSWD: ALL" | sudo tee /etc/sudoers.d/prodadmin
#### Next, run hardening
 ANSIBLE_CONFIG=inventories/prod/ansible.cfg ansible-playbook playbooks/harden.yml -l prod_main
#### (Optional) Upgrade to version from version 7.x if needed. There is a known bug that causes PVE 8.x installation to freeze. Therefore, install 7.x first and then upgrade to 8.x via below command.
ANSIBLE_CONFIG=inventories/prod/ansible.cfg ansible-playbook playbooks/upgrade-to-pve8.yml -l prod_main --ask-vault-pass
#### Run a basic check, “changed” means passed.
ANSIBLE_CONFIG=inventories/prod/ansible.cfg ansible-playbook playbooks/check-basics.yml -l prod_main
## To create new ansible-role folder structure
ansible-galaxy init ansible/roles/role-name/
## Print Server CUPS
### VM Setup
#### To set up CUPS. Run the “print-server” play.
ansible-playbook playbooks/create-print-server.yml --ask-vault-pass
#### If the printer is not added properly, connect the printer via USB port and add the printer from hardware properties.
##### The set up is optimized for an EPSON ET-2850 series printer. Therfore, changes may be made to accommodate for a different series printer.
##### TODO: Add roles for automatically adding the printer via USB.
### Fine Tuning
#### Printer Side
##### Goto the printer UI and reset all settings.
##### Turn the WIFI off, we don’t need it anymore!
##### To help suppress some warnings related to page size, disable auto page size switching and then set paper size to A4.
##### Finally, save all changes.
#### Server Side
##### Navigate to server ip:631/admin. We can use server root credentials to authorize any changes.
##### Next, click “Add Printer” and pick one from local.
##### Check to share the printer if not already set bu Ansible.
##### For driver, it was found that “IPP Everywhere” works better than “Epson factory driver” or “Driverless” configuration. Also, it appears that factory driver seems to execute print job super slow!
##### Add Printer and authorize by entering the root credentials.
##### Also, make changes “Set Default Options” to change the paper size to A4 if not set already.
#### User Side
##### On a windows machine, add the printer.
##### Then go to settings to set the paper size to A4.
##### Click apply to apply all changes. This should suppress the warnings related to paper size mismatch warnings.

## Samba File Server
### HDDs structure for reference.

### Create the ZFS mirror from bulk HDDs.
ansible-playbook playbooks/create-file-server.yml --ask-vault-pass
# Routine maintenance
## <List routine maintenance procedure and intervals>
# Appendix A References
## <List continues>

# Appendix B Definitions / acronyms
TERM	MEANING	TERM	MEANING
LTS	Long Term Support

# Appendix Diagrams
# Appendix Bill of materials
## <List Bill of materials>
# Appendix D Testing Validation
## Equipment / Materials
### Equipment
#### <Equipment>
### Materials
#### <Material>
## Prerequisites
### <List prerequisites if any>
## Test configuration(s) information
Item	Configuration

## Test Instruction
Requirment#	Description	Test?	Pass?
	<First one>	Y/N	Y/N

# Appendix C Usage instruction
## <Document special usage instruction if any>

# Appendix Diagrams